## Slide 1: Low Carbon Cement: Making it happen
Sustainability Consultant
Dr Anders McCarthy
Webinar Series: Capacity Building for Industrial Partners in Pakistan
22.10.2025

## Slide 2: Mitigation Technologies

## Slide 3: Effective pathways to Decarbonise Cement NOW
The most effective way to decarbonise the cement sector TODAY is through Limestone Calcined Clay Cement (LC3)

## Slide 4: Supplementary Cementitious Materials
Scrivener et al., 2018 Cement and Concrete Research
SCMs: Reducing the clinker factor to decrease CO2 emissions by adding SCMs.
Types of SCMs: Fly ash, blast furnace slag, natural pozzolan, silica fume, rice husk ash.
Challenge: lack of sufficient high quality SCMs to reduce the clinker factor.
Alternative: Kaolinite-bearing clays which are calcined at 700-850°C + an addition of a small percentage of limestone.
LC3: Limestone Calcined Clay Cement

## Slide 5: LC3 versus OPC
LC3.ch, 2022, LC3: A sustainable alternative for the cement industry, 2022
LC3 can decrease infrastructure costs substantially
Up to 40% decrease in GHG emissions (LC3-50)
Up to 25% cheaper to produce
Zunino & Scrivener October 2025 CBM: LC3 with 25-35% clinker shows potential for high strength and general use cement.
High upfront costs requires Concessional and Carbon Finance

## Slide 6: An Enabling Environment for Low-Clinker Cement and Concrete
Target:
Address demand-side barriers to unlock private & public sector investments.
Update cement and concrete standards to allow for the use of low-clinker cements. E.g., EN 197-5, PS 5586:2023, ASTM C595, IS 18189:2023.
Barrier 1
Development and Adoption of Standards
Barrier 2
Green Building Code Amendments
Barrier 3
Green Public Procurement Reform
Updating Building Codes to prevent the overuse of OPC and stimulate the use of low-clinker cements/concrete.
Green Public Procurement criteria to prioritize the use of low-clinker cements and concrete.
For transformational change that attracts financing opportunities, commitment from relevant authorities who develop and implement standards, building codes and procurement policies is essential. This would strengthen the case of cement companies to access financing.

## Slide 7: Financing: Getting Started

## Slide 8
406 projects developed worldwide:
Clinker Substitution
Energy Efficiency
Waste Heat Recovery
CDM Pipeline Database, filtered for Projects which have been validated, registered. (as of December 2024)
GHG methodologies well developed over the years:
e.g., ACM0003, AMSIII.Q,
Chart: Historical Cement CDM Projects
| China | India | Mexico | Colombia | Thailand | Philippines | Jamaica | Syria | Dominican Republic | Indonesia | Argentina | Armenia | Brazil | Cambodia | Egypt | Honduras | Israel | Kenya | Libya | Pakistan | South Korea | United Arab Emirates | Vietnam
 | 280 | 55 | 10 | 3 | 15 | 2 | 1 | 1 | 3 | 3 | 1 | 1 | 1 | 1 | 4 | 2 | 2 | 1 | 1 | 12 | 1 | 3 | 3
Cement Sector Experience under CDM
Waste Heat Recovery at Attock Cement Plant (Baluchistan)
Cement is a key sector through which Carbon Finance can be efficiently implemented as every part of the value chain can be easily monitored (MRV), ensuring transparency and high integrity of internationally transferred mitigation outcomes (ITMOS) delivered.
Waste co-processing remains a key methodological challenge!

## Slide 9
Financing pathways for the cement sector
Cement Decarbonisation Project
Concessional Finance
Grant (Technical Assistance)
Article 6 – Carbon Finance
In 2024, MOCC&EC published the Carbon Market Guidelines. A Carbon Market Watch Group (CMWG) and a digital National Carbon Registry will be developed to facilitate the implementation of Article 6 projects.
MDBs, DFIs wishing to catalyse private sector investments
Bilateral partners willing to purchase ITMOs
SPAR6C ToolBox : Screening and developing Article 6 activities
Not Viable under current market conditions

## Slide 10
Step 1: Project Idea Note (PIN)*
See Annex 1 & 2 of the Carbon Market Guidelines & Chapter 3 of the Screening and Developing Article 6 Activities
PIN can then be shared with potential ITMO-acquiring parties as well as MoCC&EC (NDA - National Designated Authority) for approval and issuance of a Letter of Intent.
Identify all costs and revenue streams: Capex, Opex, Revenue, Energy/Tax Savings
Assessment of Financial viability and demonstration of Additionality.
* Also called Mitigation Activity Idea Note (MAIN)

## Slide 11
Step 2: Project Design Document**
This is a fully developed PIN. This updated PDD has additional (NEW) requirements compared to CDM.
Important: Needs to be in line with NDC, align with Government Sustainable Development Policies and needs to show a transformational change.
Chapter 4 of the Screening and Developing Article 6 Activities
ITMO-buying entities (donor countries) and private foundations can provide upfront financing for the development of a full PDD with the help of external consultants.
** Also called Mitigation Activity Design Document (MADD)

## Slide 12
Step 3 & 4: Validation and Implementation
Step 3: Validation & Approval
The project will be validated by qualified, independent third-party auditors – Designated operational entities (DOE). This step, where costs vary substantially based on the project, assess the validity of the assumptions and calculations + sustainable development co-benefits.
Only once the PDD is validated can the project be approved and then implemented.
Chapter 5 & 8 of the Screening and Developing Article 6 Activities
Typical challenges for validation include : lack of engagement with all stakeholders, insufficient evidence for additionality, MRV is unclear, and unclear baseline.
Step 4: Implementation and MRV
Ensuring transparency and high integrity of internationally transferred mitigation outcomes (ITMOS) requires a well-designed Monitoring activity for GHG emissions and good QA/QC.

## Slide 13
Request upfront grant financing (TA) to address demand-side levers/barriers.
Long-term Vision: Sectoral Approach
Certain ITMO-buying entities are interested in transformative sector-wide projects.
II) Based on pilot-projects implemented, expanding to a Cement Sectoral Approach could be possible.
WHR
LC3
Waste
Solar PV/BESS
Sectoral Financing Instrument for Green Cements
PDD, letter of no objection
Concessional Finance
(MDBs, IFDs)
Carbon Finance from ITMO-buying entities
Carbon Payment
(X USD/Ton)
Emission Reduction Units, Standardized GHG Monitoring System
iii) A Sectoral Financing Instrument would simplify submission process per individual project.
IV) Establishing a mandatory, standardized GHG monitoring system, along with developing a sector-wide Marginal Abatement Cost Curve (MACC) would ensure data consistency & investment prioritization.

## Slide 14
Thank you
Contact information
Dr. Anders McCarthy
Heat International
mccarthyanders@gmail.com